## Slide 1: U3_L1_ALL2
Class: 5 CM/TL Prof. Massimo Eccher
School year: 2017-18
Aerodynamics and Airfoils

## Slide 2: WINGS and AIRFOILS
An airfoil is the shape of a wing.
An airfoil-shaped body moved through a fluid produces an aerodynamic force.
Adapted from: http://www.aerospaceweb.org/question/design/q0101.shtml

## Slide 3: HELP ME with AIRFOIL TERMINOLOGY
Mean Chamber Line: Set of points halfway between ….. and ……surfaces
  measured perpendicular to mean chamber line itself
Leading Edge: Most forward point of mean …..
Trailing Edge: Most reward point of mean …….
Chord Line: Straight line connecting …….
Chord, c: Distance along the chord line ….. to trailing edge
Camber: ……. distance between ……line and …… line
measured perpendicular to chord line
Adapted from: http://www.aerospaceweb.org/question/design/q0101.shtml

## Slide 4
“Tell me everything can you about the design of these wings…”

dihedral
All images are licensed under BY Creative Commons.

## Slide 5: THE AERODYNAMIC FORCE ON A WING
Relative Wind: Direction of V∞
    We used subscript ∞ to indicate far upstream conditions
Angle of Attack, a, Angle between relative wind (V∞) and chord line
Total aerodynamic force, R, can be resolved into two force components
    Lift, L: Component of aerodynamic force perpendicular to relative wind
    Drag, D: Component of aerodynamic force parallel to relative wind
https://aviation.stackexchange.com/questions/28019/what-factors-determine-the-direction-of-the-resultant-force-vector

## Slide 6: RESOLVING THE AERODYNAMIC FORCE: ROCKET
Aerodynamic force, R, may also be resolved into components perpendicular and parallel to chord line
  Normal Force, N: Perpendicular to chord line
  Axial Force, A: Parallel to chord line
L and D are easily related to N and A
For airfoils and wings, L and D most common
For rockets, missiles, bullets, etc. N and A more useful
https://aviation.stackexchange.com/questions/28019/what-factors-determine-the-direction-of-the-resultant-force-vector

## Slide 7: VARIATION OF L, D, AND M WITH a
Lift, Drag and M on a airfoil or wing will change as a changes
Variations of these quantities are some of most important information that an airplane designer needs to know
Aerodynamic Center
  Point about which moments essentially do not vary with a
  Mac=constant (independent of a)
  For low speed airfoils aerodynamic center is near quarter-chord point

## Slide 8: SAMPLE DATA: SYMMETRIC AIRFOIL
Lift Coefficient
Angle of Attack, 
A symmetric airfoil generates zero lift at zero a
Adapted from: https://www.quora.com/How-is-lift-generated-with-symmetrical-wings

## Slide 9: SAMPLE DATA: CAMBERED AIRFOIL
Lift Coefficient
Angle of Attack, 
A cambered airfoil generates positive lift at zero a
Adapted from: https://www.quora.com/How-is-lift-generated-with-symmetrical-wings

## Slide 10: WHY DOES LIFT CURVE BEND OVER?
Source: http://www.formula1-dictionary.net/coanda_effect.html
NO LIFT
FLIGHT
STALL