## Slide 1: U3_L2_ALL6
Class: 5 CM/TL Prof. Massimo Eccher
School year: 2017-18
Effects of Viscosity

## Slide 2
Summary
Viscous flows
Laminar vs turbulent flows
Reynolds number
Flow separation
Airfoil stall

## Slide 3: REAL EFFECTS: VISCOSITY ()
To understand drag and actual airfoil/wing behavior we need an understanding of viscous flows.
Inviscid (frictionless) flow around a body will result in zero drag!
Do all real flows have friction?

## Slide 4
Flow adheres to surface because of friction between gas and solid boundary. Thin region of retarded flow in vicinity of surface, called a ‘Boundary Layer’
    At outer edge of B.L., V∞
    At solid boundary, V=0
Source: https://leehamnews.com/2018/01/05/bjorns-corner-aircraft-drag-reduction-part-11/
BOUNDARY LAYER

## Slide 5: COMMENTS ON VISCOUS FLOWS
Velocity profile through a boundary layer
https://en.wikipedia.org/wiki/Boundary_layer_thickness
Boundary layer
Surface
Outer edge of boundary layer

## Slide 6: TYPES OF FLOWS: FRICTION VS. NO-FRICTION
http://www.zoombd24.com/boundary-layer-control-airfoil-boundary-layer-separation-control-devices-details
Flow very close to surface of airfoil is
Influenced by friction and is viscous
(boundary layer flow)
Stall (separation) is a viscous phenomena
Flow away from airfoil is not influenced
by friction and is wholly inviscid
https://people.rit.edu/pnveme/MECE409/Images/FlowClassification.html

## Slide 7
Two types of viscous flows
  Laminar: streamlines are smooth and regular and a fluid element moves smoothly along a streamline
  Turbulent: streamlines break up and fluid elements move in a random, irregular, and chaotic fashion
Laminar flow
Turbulence
Transition
https://www.quora.com/Which-is-better-in-a-heat-transfer-laminar-flow-or-turbulent-flow

## Slide 8: LAMINAR VERSUS TURBULENT FLOW
All B.L.’s transition from laminar to turbulent
Turbulent velocity profiles are ‘fuller’
https://www.cfdsupport.com/OpenFOAM-Training-by-CFD-Support/node279.html
Notes: Dopo la prima parte dell impatto, il flusso diventa turbolento
Il boundary layer turbolento è piu spesso (delta turb)

## Slide 9
Velocity boundary layer development on a flat plate.
https://physics.stackexchange.com/questions/281281/about-the-definition-of-boundary-layer

## Slide 10
Boundary layers can be either laminar or turbulent.
A reasonable assessment of whether the boundary layer will be laminar or turbulent can be made by calculating the Reynolds number of the local flow conditions.
LAMINAR VERSUS TURBULENT FLOW

## Slide 11: THE REYNOLDS NUMBER, Re
Reynolds number is ratio of two forces:
  Inertial Forces
  Viscous Forces
  l is length scale (chord)
Reynolds number tells you when viscous forces are important and when viscosity may be neglected
Within B.L. flow
highly viscous
(low Re)
Outside B.L. flow
Inviscid (high Re)
http://www.zoombd24.com/boundary-layer-control-airfoil-boundary-layer-separation-control-devices-details

## Slide 12
What causes flow separation?
https://en.wikipedia.org/wiki/Flow_separation

## Slide 13: FLOW SEPARATION
Friction causes flow separation within boundary layer
Separation then creates another form of drag called pressure drag due to separation
https://en.wikipedia.org/wiki/Flow_separation

## Slide 14: COMPARISON OF DRAG FORCES
d
d
Same total drag as airfoil
http://www.aerospaceweb.org/question/aerodynamics/q0215.shtml

## Slide 15: OVERVIEW: AIRFOIL STALL
Friction causes flow separation within boundary layer
  B.L. either laminar or turbulent
  All laminar B.L. → turbulent B.L.
  Turbulent B.L. ‘fuller’ than laminar B.L., more resistant to separation
Separation creates another form of drag called pressure drag due to separation
  Dramatic loss of lift and increase in drag
https://commons.wikimedia.org/wiki/File:1915ca_abger_fluegel_(cropped_and_mirrored).jpg

## Slide 16: WHY DOES BOUNDARY LAYER SEPARATE?
Graphical representation of the velocity profile in the boundary layer.
Flow separation occurs when the BL travels far enough against an adverse pressure gradient that the speed of the BL relative to the object falls almost to zero.
The fluid flow becomes detached from the surface of the object, and instead takes the forms of eddies and vortices.
https://commons.wikimedia.org/wiki/File:Boundary_layer_separation.svg

## Slide 17
Airflow separating from a wing at a high angle of attack

## Slide 18: Why does an airfoil stall?
https://en.wikipedia.org/wiki/Stall_(fluid_mechanics)

## Slide 19: WHY DOES AN AIRFOIL STALL?
Two undesirable consequences of separated flow over airfoil
  Dramatic loss of lift (stalling)
    Separated flow causes higher pressure on upper surface of airfoil
  Major increase in drag
    Separation causes lower pressure on trailing edge
    Unbalance of pressure force causes pressure drag due to separation

## Slide 20
Inclination effects
https://www.grc.nasa.gov/www/k-12/airplane/incline.html

## Slide 21: SAMPLE DATA: CAMBERED AIRFOIL STALL
Lift or Lift Coefficient
Angle of Attack, 
https://answers.unity.com/questions/910684/how-to-create-interactive-fluid-effect.html
https://en.wikipedia.org/wiki/Flow_separation